## Slide 1: Exercise 1: Basic Input
Beginners FLUKA Course

## Slide 2: Exercise 1: Basic Input
Proton beam impinging on a cylinder of pre-def material
Get the source example files from the course website
http://www.fluka.org/fluka.php?id=course&sub=program&which=demokritos2009
Download all the ex1*.inp files to ~/work/ex1 directory
Different input formats:
ex1.inp fixed card format free geometry format (RECOMMENDED)
ex1free.inp free card format free geometry format
obsolete (but supported)
ex1fix.inp fixed card format fixed geometry format (DEFAULT)
ex1double.inp fixed card format high-accuracy fixed geometry format
ex1fixfree.inp free card format fixed geometry format

## Slide 3: Exercise 1: Basic Input
run ex1.inp in the ex1 dir
$$FLUPRO/flutil/rfluka –N0 –M4 ex1 &
look at the .out file
$emacs [or any editor] ex1001.out &
find the inelastic scattering length for beam particles in the target
determine how many primaries are needed to have a run (with 4 cycles) lasting in total as many minutes as the number of neutrons of the 6He’s isotope
find the fraction of energy leaving the system
calculate the power leaving the system for a beam current of 4mA (in S.I. units)