## Slide 1
FLUKA Beginner’s Course
Low Energy Neutrons

## Slide 2: Introduction
In FLUKA we call neutrons below 20 MeV low energy neutrons
Neutron interactions at higher energy are handled by FLUKA nuclear models
Transport and interactions of neutrons with energies below 20 MeV are handled by a dedicated library
Why are low Energy Neutrons special?
The neutron has no charge  can interact with nuclei at low energies, e.g. meV
Neutron cross sections () are complicated  cannot be calculated by models  we rely on data files

## Slide 3: Typical neutron cross section
tot
thermal  1/v
unresolved resonance region
resolved
resonance
region
Ekin incident neutron
1eV
1keV
1MeV
Resonances  energy levels in compound nucleus A+1Z*
resonance
spacing
few eV
Resonance spacing too dense  overlapping resonances

## Slide 4: Evaluated Nuclear Data Files
Evaluated nuclear data files (ENDF, JEFF, JENDL...)
  typically provide neutron  (cross sections) for E<20MeV for all channels
   are stored as continuum + resonance parameters
  Point-wise and Group-wise cross sections
In neutron transport codes in general two approaches are used: point-wise (“continuous” cross sections) and group-wise transport
Point-wise follows cross section precisely but it can be time and memory consuming
Group approach is widely used in neutron transport codes because it is fast and gives good results for most application
Complex programs (NJOY, PREPRO...) convert ENDF files to point-wise or group-wise cross sections, including Doppler broadening etc.

## Slide 5: Group Transport Technique
The energy range of interest is divided in a given number of discrete intervals (“energy groups”). Each group is identified by a number increasing with decreasing energy. Group 1 is the group of highest energy (in the present FLUKA library, energies between 19.64 and 20 MeV)
Elastic and inelastic reactions are not simulated as exclusive processes, but by group-to-group transfer probabilities (downscattering matrix)
Downscattering matrix: if a neutron in a given group undergoes a scattering event and loses energy, it will be transferred to a group of lower energy (each of the lower energy groups having a different probability)
If the neutron does not lose enough energy to be in another group, it will stay in the same group (in-scattering)
In the thermal region neutrons can gain energy. This is taken into account by an upscattering matrix, containing the transfer probability to a group of higher energy
Notes: Add maybe a picture of group cross sections

## Slide 6: Angular distribution [1/2]
The probability distribution of the scattering angle for each group-to-group transfer is represented by a Legendre polynomial expansion truncated at the (N+1)th term:
where

## Slide 7: Angular distribution [2/2]
In FLUKA, N=5
The scattering angular probabilities are obtained by a discretization of a P5 Legendre polynomial expansion of the actual scattering angular distribution which preserves its first 6 moments.
Result of this P5 expansion is a set of 3 discrete polar angle cosines and 3 corresponding probabilities, i.e. for a given transfer gg’ only three values are possible for the polar angle
The azimuthal angle is sampled from a uniform distribution and can have any value between 0 and 2

## Slide 8: Group wise treatment
Convert  to energy groups like histograms, the energy width is different for each group in order to better represent resonances
Each group i contains the <average> i :
where F is the fluence
Advantage: fast
Disadvantage: effects like self shielding are not accurately reproduced
(see later), angular distributions replaced by a discrete number of
angles (3 in FLUKA) conserving their first n moments (6 in FLUKA)

## Slide 9: Fluence
An assumption is needed about the neutron spectrum to be used as a weighting function for calculating the average cross section on each group
For instance it can be shown that in most cases, between 1 eV and 1 MeV:
E*(E)
logE (lethargy)
1eV
1keV
1MeV
Isolethargic distribution
Maxwell-distribution
displayed in lethargy plot
Eth
Shape determined
by thermal motion
of nuclei (depends on
temperature)
(
spectrum)
In any case, the error is small if the group width is small

## Slide 10: Self shielding
The group structure is necessarily coarse with respect to the resonance structure in many materials
A resonance in a material present in a dilute mixture or as a small piece cannot affect much a smooth neutron flux (so-called “infinite dilution'')
But if an isotope exhibiting large resonances is very pure or is present with a large fractional abundance, it can act as a “neutron sink”, causing sharp dips in the neutron spectrum corresponding to each resonance  an apparent decrease in σ
This effect, which results in a lower reaction rate , is called self-shielding and is necessarily lost in the process of cross section averaging over the width of each energy group, unless a special correction is made

## Slide 11: The FLUKA Low Energy Neutron Library [1/3]
FLUKA uses the multigroup transport technique
The energy boundary below which multigroup transport takes over depends in principle on the cross section library used. In the present library it is 20 MeV.
Both fully biased and semi-analog approaches are available
Number of groups: 260 of approximately equal logarithmic width, the actual energy limits of each group can be found in the manual (or can be printed to *.out file)
N.B. the group with the highest energy has the number 1, the group with the lowest energy has number 260
31 thermal groups, with 30 upscattering groups
Energy range of library: 0.01 meV - 20 MeV

## Slide 12: The FLUKA Low Energy Neutron library [2/3]
Based on recent versions of evaluated nuclear data files: ENDF/B-VI.8, ENDF/B-VII.0, Jendl-3.3, Jendl-3.4, Jeff-3.1,…
About 270 isotopes/materials available
Almost all materials available at 2 temperatures: 87K, 296K
Some also at 4K, 120K, 430K
Doppler broadening at the relevant temperature is taken into account
The library handles also gamma generation, energy deposition by kerma factors, residual nuclei production, secondary neutrons, fission neutrons
For some isotopes/materials: self-shielding, molecular binding, correlated gamma generation, point-wise transport
NB: Because of the group technique the energy of a transported neutron below 20 MeV is only defined within the resolution of the groups

## Slide 13: The FLUKA Low Energy Neutron library [3/3]
Energy weighting:
Averaging inside each energy group according to the following weighting function. In order of increasing energy:
  a Maxwellian at the relevant temperature in the thermal range
  a 1/E spectrum in the intermediate energy range
  a fission spectrum
  again a 1/E spectrum
But it is important to realize that the groups in the present library
are very narrow! Therefore the energy weighting is not very
important

## Slide 14: Gamma generation
Gamma generation from (n,x) reactions is possible only for those elements for which data are available in the evaluated nuclear data files (see manual for a complete list)
Gamma generation is performed by a multigroup scheme as well
Number of gamma groups: 42
  NB number of  groups different from number of neutron groups!
Energy range: 1keV - 50 MeV
  NB  energy range different from neutron energy range!
The actual energy of the generated photon is sampled randomly in the energy interval corresponding to its gamma group
Exception: 2.2 MeV from H(n,)2H reaction, 478 keV photon from 10B(n, g) and gamma cascades from Cd(n,) and Xe(n,)
Capture gammas as well as gammas from inelastic reactions like (n,n’) are included
The neutron library only creates gammas, the transport is done by the EMF module (like all other gammas in FLUKA)

## Slide 15: Energy deposition
Energy deposition by neutrons below 20 MeV is estimated by means of kerma factors
For some materials with gamma production the kerma values of some groups (mainly at high energies) are problematic (see manual). The reason is inconsistent data in the evaluated data files. Effort was addressed to apply corrections to improve the situation but there are still some materials with problematic kermas.
The user should check carefully the results of simulations with these materials. However, the effect should vanish in a typical simulation.

## Slide 16: Secondary and Fission Neutrons
Neutrons from (n,xn) reactions are taken into account implicitly by a group-dependent non-absorption probability, i.e. a factor by which the weight of a neutron is multiplied after a collision
If the only possible processes are scattering and capture the non-absorption probability is smaller than 1. If also (n,2n) is possible, the factor is bigger than 1
Fission neutrons are treated separately by a group-dependent fission probability
Fission neutrons are emitted isotropically with an energy sampled from a fission spectrum appropriate for the isotope and neutron energy
The fission neutron multiplicity was obtained separately from the evaluated data files
The fission fragments are not transported, their energy is deposited at the spot

## Slide 17: Charged particle generation
Recoil protons from hydrogen and protons from 14N(n,p) are produced and transported explicitly (i.e. like other protons)
That means that detailed kinematics of elastic scattering, continuous energy loss with energy straggling, delta ray production, multiple and single scattering, are all taken into account
If point-wise transport has been requested,  and 3H fragments from neutron capture in 6Li and 10B can also be transported explicitly
Note that for this purpose you cannot use the cross sections of natural Li and B, but you must define a compound of 6Li and 7Li, or one of 10B and 11B
All other charged secondaries produced in low energy neutron reactions are not transported but their energy is deposited at the point of interaction using kerma factors
Notes: Is it true for 10B?

## Slide 18: Residual nuclei production
Residual nuclei: nuclei that are the result of a reaction and are at rest, e.g. 28Al after a neutron capture reaction of 27Al
For all materials data are available for estimating residual nuclei production by low energy neutrons. Command RESNUCLEi allows to request separately residual nuclei from low energy neutrons and from high energy particles
For Ti, Ga the residual nuclei information is based on different evaluations than the transport

## Slide 19
Using the
Low Energy Neutron Library

## Slide 20: Available Materials
Section 10.4.1.2 of manual gives a list of available materials
Example:
RN: residual nuclei
Gam: Gamma production
Name: name to be used in LOW-MAT card
Identifiers: to be used in LOW-MAT card
Notes: Put the complete list at the end

## Slide 21: Using the Low Energy Neutron Library
How to activate low energy neutron transport?
  Implicit: giving a DEFAULTS cards (except with default EM-CASCA), or not giving a DEFAULTS card at all
  That means: you are using the library in almost any simulation (unless you are using the default EM-CASCA or you have switched it off explicitly with a LOW-BIAS or PART-THR card)
  Explicit: giving a LOW-NEUT card
    NB you don’t need it in most practical cases! (See below)
What must the user do?
  To set correspondence between the actual material and the material in the low neutron library (LOW-MAT card), if not done by default.
    NB you don’t need it in most practical cases!
  To set transport thresholds with PART-THR, if defaults are not ideal for the actual problem
  To request special features like point wise cross sections or cross section printing (LOW-NEUT)

## Slide 22: Input Cards: LOW-NEUT [1/4]
This card activates low-energy neutron transport.
WHAT(1): number of neutron groups of the library
  Default: 260
WHAT(2): number of gamma groups of the library
  Default: 42
WHAT(3): maximum energy (in GeV) of the library
  Default: 0.02
WHAT(5): number of thermal groups
  Default: 31
The defaults for WHAT(1) – WHAT(3) and WHAT(5) are fine. The only reason for changing them would be if using a different library (there was one until recently, but it has been suppressed)
 Don’t use them!

## Slide 23: Input Cards: LOW-NEUT [2/4]
WHAT(4): printing flag, neutron cross section information is written to *.out file
    0.0 Minimum
    1.0 integral cross sections, kerma factors and probabilities
    2.0 additionally downscattering matrices and gamma matrices
    3.0 additionally scattering probabilities and angles
    4.0 residual nuclei information
  Default: 0.0 (minimum)

## Slide 24: Input Cards: LOW-NEUT [3/4]
The output for WHAT(4) = 1
  Group energy limits, average energies, velocities and momenta, thermal velocities, gamma group limits
  For each material: availability of residual nuclei information ( the line: “RESIDUAL NUCLEI INFORMATIONS AVAILABLE” indicates the possibility to use option RESNUCLEi with WHAT(1)= 2.0
  for each neutron energy group in each material:
    SIGT = total cross section
    SIGST = “scattering” cross section: s(n,n) + 2s (n,2n) + 3s (n,3n)
    PNUP = upscatter probability, is 0.0 in non thermal groups
    PNABS = Probability of Non-ABSorption (= scattering) PNABS = SIGST/SIGT, and can sometimes be> 1 because of (n,xn) reactions
    GAMGEN = GAMma GENeration probability = gamma production cross section divided by SIGT and multiplied by the average number of g per (n, g) reaction
    NU*FIS = fission neutron production = fission cross section divided by SIGT and multiplied by , the average number of neutrons per fission
    EDEP = Kerma contribution in GeV per collision
    PNEL, PXN, PFISS, PNGAM = partial cross sections, expressed as probabilities (i.e., ratios to SIGT). In the order: non-elastic, (n,xn), fission, (n,gamma)
Notes: Skip LOW-NEUT:WHAT(4) =2 and WHAT(4)=3, but maybe angles are important

## Slide 25: Input Cards: LOW-NEUT [4/4]
WHAT(6): i0 + 10 * i1:
  i0 = 1: available point wise cross sections used and explicit and correlated 6Li(n,)7Li, 6Li(n,t)4He, 10B(n,ag)7Li, 40Ar(n, ) 41Ar, xXe(n, ) x+1Xe and 113Cd(n, )114Cd photon cascade requested
    = 0: ignored
    =< -1: resets to the default (point wise cross sections are not used)
  i1 = 1, fission neutron multiplicity forced to 1, with proper weight to compensate for the “wrong” multiplicity
    = 0, ignored
    =< -1: resets to the default (normal fission multiplicity)
  Default = -11., unless option DEFAULTS is present with SDUM = CALORIME, ICARUS, NEUTRONS or PRECISIO, in which case the default is 1.0 (point wise cross sections are used when available and fission multiplicity is not forced)

## Slide 26: Input Cards: LOW-MAT [1/3]
The LOW-MAT card sets the correspondence between FLUKA materials and the low energy neutron cross sections
If a material has the same name as a name given in the list of low neutron materials, the correspondence between material and low energy neutron transport is set automatically, and a LOW-MAT card is not necessary. The first material with the right name is taken. This is always a material at room temperature.
That means that for the predefined material HYDROGEN hydrogen bound in water is used, not the free gas one
If you want to use low energy neutron transport in H2 gas you have to do this explicitly by a LOW-MAT card

## Slide 27: Input Cards: LOW-MAT [2/3]
WHAT(1): Name of the material (single element/isotope only!)
    In flair this can be chosen from a pull down menu
WHAT(2), WHAT(3) and WHAT(4): the 3 identifiers from table 10.4.1.2 of the manual
SDUM: name of the material from table 10.4.1.2 of the manual
In flair there is only one pull down menu for all identifiers and the name
If you want to use the predefined materials at a temperature different from 296K, it is mandatory to give a LOW-MAT card with the proper identifiers
Notes: Picture LOW-MAT card

## Slide 28: Input Cards: LOW-MAT [3/3]
Setting the correspondence between a material and low energy neutron transport cross sections:
  First create the material with a MATERIAL card and give it a name in SDUM
  Give a LOW-MAT card with WHAT(1) = the name you gave in the SDUM of the MATERIAL
  Give in WHAT(2), WHAT(3) and WHAT(4) of the LOW-MAT card the numerical identifiers (table 10.4.1.2 in manual) of the material you want to use, be careful to use the one with the right temperature
  Give in SDUM of the LOW-MAT card the name provided in the same table

## Slide 29: Example: compound at 87K
Example: sodium iodide (NaI) at 87K
  Create a material sodium and give it some name (SODIU_87), do the same with iodine (IOD_87)
  Give a LOW-MAT card for SODIU_87, choose the right cross sections identifiers (those for 87K) and name (see list in manual), do the same for iodine
  Create a material NAI_87 by giving first a MATERIAL card and then a corresponding COMPOUND card with the right composition

## Slide 30: Input Cards: LOW-BIAS [1/2]
This card sets an energy cut-off during low-energy neutron transport on a region by region basis and/or non-analog absorption.
However, for an overall energy cut-off, it is preferable to use PART-THR
WHAT(1): number of the group to apply a transport cut-off, i.e. neutrons in groups the number of which >= WHAT(1) are not transported. Remember that the group with the highest energy has the number 1.
  Default: 0.0 (no cut-off)
  flair automatically matches the group number to the upper energy boundary of each group

## Slide 31: Input Cards: LOW-BIAS [2/2]
Analog absorption: a neutron does not exist any more after an absorption process
Non-analog absorption: the neutron is never killed at any interaction, but lives on with a lower weight, accounting for the relative probability of absorption and scattering.
Capture gammas are created with a weight equal to that of the surviving neutron
WHAT(2): Group limit for non-analog absorption (neutrons in groups >= WHAT(2) undergo non-analog absorption)
  Default: 230 (non-analog absorption for all thermal neutrons)
WHAT(3): non-analog survival probability
  Default : 0.85 or 0.95, DEFAULTS-dependent)
WARNING: Only experts should modify the non-analog absorption survival probability!
If no LOW-BIAS card is given, non-analog absorption depends on the DEFAULTS card (see manual)
The change of weight of the particle is taken into account (see lecture about biasing)

## Slide 32: Transport cut-offs
Transport cut off: a particle is not transported if its energy is lower than a cut off energy
Transport cut offs for neutrons can be set to save CPU time
Use cut offs with care, you could miss important effects like activation, dose, secondary particles,…
For activation, thermal neutrons are very important. If you are interested in activation never cut off low energy neutrons!
To set a general transport cut off for neutrons, please give the energy of the cut off in the PART-THR card, no matter if high or low energy neutrons. That was different in previous versions: the card LOW-BIAS was needed for low energy neutrons. LOW-BIAS is still needed if one wants set a cut-off region by region
If there is no interest in low-energy neutron transport, but that feature is implicit in the DEFAULTS option chosen, it is suggested to request LOW-NEUT, and to use PART-THRes with an energy cutoff WHAT(1) = 0.020

## Slide 33: Self-shielding [1/3]
Self-shielded materials in FLUKA:
  27Al at 296K, 87K, 4K, 430K
  natA, 40Ar at 296K, 87K
  natFe at 296K, 87K, 4K, 430K
  natCu at 296K, 87K, 4K, 430K
  181Ta at 296K, 87K
  natW at 296K, 87K, 4K, 430K
  197Au at 296K, 87K
  natPb at 296K, 87K
  208Pb at 296K
  209Bi at 296K, 87K
    Special case: cast iron (natFe +5%C) at 296K, 87K, 4K, 430K (see example further on)

## Slide 34: Self-shielding [2/3]
When to use these materials?
  Bulky (huge) pieces that are very pure (containing only one isotope)
When not to use self-shielded materials?
  “small” iron, copper, lead, aluminum pieces
  Thin gold foils (but a self-shielded 100mm Au foil is available)
  Diluted materials
How to use self-shielded materials?
  Define your material with a MATERIAL card
  Give additionally a LOW-MAT card and give the proper identifiers in WHAT(2)-WHAT(4) and SDUM
  If you have to use self-shielded and non self-shielded materials of the same element you need to define 2 different materials
  Attention: predefined materials like iron, copper and lead are not self-shielded, you have to give a LOW-MAT card to use them self- shielded

## Slide 35: Self-shielding [3/3]
Cast iron is iron with a significant amount of carbon
There is a self-shielded material cast iron in the low energy neutron library which is prepared to be used for creating a compound of iron and roughly 5% carbon. The amount of carbon doesn’t need to be exactly 5%.
How to create self-shielded cast iron?
  Define a material iron called FeCarbSS (or any other name you like) with a MATERIAL card (parameters as for natural iron)
  Insert a LOW-MAT card for FeCarbSS with the proper identifiers for cast iron in WHAT(2)-WHAT(4) and SDUM
  Insert a MATERIAL card to declare a compound material called CastFe (or any other name you like)
  Insert a COMPOUND card for defining CastFe as a compound of FeCarbSS and CARBON (predefined)

## Slide 36: Artifacts of discrete angular distribution
Artifacts can arise when a neutron is likely to scatter only once (thin foil, regions of low density like gases), due to the discrete angular distribution (only 3 angles are possible for each gg’)
The user should be aware of such artifacts and interpret results of scattering at thin foils and gases carefully
Because the 3 angles are different for each gg’ and the azimuthal angle is sampled from a continuous distribution, the artifact disappears when the neutrons have the possibility of scattering two or more times.
Information about which angles and probabilities are used for each group can be obtained by setting WHAT(4) = 3 in the LOW-NEUT card. The information is then written to the *.out file (see manual chapter 9: Output)

## Slide 37: Materials with molecular binding
Available materials with molecular bindings at 296K:
  H (natural isotopic amount) in H2O, CH2
  1H in H2O, CH2
  2D in D2O
  C in graphite
Use of these materials makes the thermal neutron calculation more realistic and can affect the energy and spatial distributions
Example: CH2 (polyethylene) including molecular binding
  Create a material hydrogen and give a corresponding LOW-MAT card that refers to H bound in CH2
  Give a COMPOUND cart that creates CH2 as a compound of bound H and normal carbon
For hydrogen, H bound in water is the default, because it is the first in the list of low energy neutron materials

## Slide 38: Advanced low energy neutron features:
The LOW-DOWN card biases the downscattering probability during low-energy neutron transport on a region by region basis
  It can be useful for very particular problems
  If not used properly it can lead to big errors
  Only recommended for experts!
Notes: MAT-PROP can be important in new library

## Slide 39: Summary
Most of the simulations in FLUKA use the low energy neutrons, implicitly via the DEFAULTS card
Low neutron transport in a material is enabled by a LOW-MAT card, only needed if the material’s name is not one of those in the neutron cross section library, or temperature, self-shielding or molecular binding are different from the default ones
Use self-shielded materials properly for “bulky” and “pure” (in isotopic composition) materials
Don’t give a LOW-MAT card for compounds