## Slide 1
FLUKA Beginner’s Course
Hadronic Interactions

## Slide 2: Hadronic showers: many particle species, wide energy range
100 GeV p in a Fe absorber:
space-averaged particle spectra
100 GeV p on Pb
shower longitudinal development

## Slide 3: Hadronic showers: we want to simulate also what is left !
The MC should be able to reproduce this complexity, maintaining correlations and cross-talks among the shower components
Hadronic interactions have to be simulated over a wide energy range with an high degree of accuracy
Nuclear effects are essential
=> need detailed nuclear interaction models
=> need checks on simple data (thin target)
A summary of the hadronic interaction models used in FLUKA is given in the following
Residual nuclei distribbution
Following 15 GeV proton interactions on Lead

## Slide 4: The FLUKA hadronic Models
Elastic,exchange
Phase shifts
data, eikonal
P<3-5GeV/c
Resonance prod
and decay
low E π,K
Special
High Energy
DPM
hadronization
hadron
hadron
Hadron-nucleus: PEANUT
Sophisticated
G-Intranuclear Cascade
Gradual onset of Glauber-Gribov multiple interactions
Preequilibrium
Coalescence
Evaporation/Fission/Fermi break-up
 deexcitation

## Slide 5: Hadron-nucleon interaction models
p-p and p-n cross section
FLUKA and data
total
elastic
Elastic, charge exchange and strangeness exchange reactions:
• Available phase-shift analysis and/or fits of experimental differential data
• At high energies, standard eikonal approximations are used
Particle production interactions: two kinds of models
Those based on “resonance” production and decays, cover the energy range up to 3–5 GeV
Those based on quark/parton string models, which provide reliable results up to several tens of TeV

## Slide 6: Nonelastic hN interactions at intermediate energies
All reactions are thought to proceed through channels like:
h + N  X  x1 + … + xn  …
h + N  X + Y  x1 + … xn + y1 + … ym  …
where X and Y can be real resonances or stable particles (, n, p, K) directly
(the intermediate state contains at least one resonance)
Resonances can be treated as real particles: they can be transported and then transformed into secondaries according to their lifetime and decay branching ratios
FLUKA:  60 resonances, and  100 channels in describing p, n, , pbar, nbar and K induced reactions up to 3-5 GeV/c
Dominance of the Δ resonance and of the N∗ resonances
Resonance energies, widths, cross sections, branching ratios
from data and conservation laws, whenever possible.
Inferred from inclusive cross sections when needed
Resonance production

## Slide 7: Nonelastic hN interactions at intermediate energies
• N1 + N2 → N’ ‘1 + N’ ‘2 + π threshold at 290 MeV, important above 700 MeV,
• π + N → π ‘+ π” + N ‘ opens at 170 MeV.
Anti-nucleon -nucleon open at rest !
π-nucleon cross section
Isospin decomposition
N1 + N2 → N”1 + Δ(1232) → N1’ + N2’ + π
π + N → Δ(1600) → π’+ Δ(1232) → π’ + π“+ N’
N’1+ N2 → Δ1(1232) + Δ2(1232) → N1’ + π1 + N’2 + π2

## Slide 8: Inelastic hN at high energies: (DPM, QGSM, ...)
Problem: “soft” interactions → QCD perturbation theory cannot be applied.
Interacting strings (quarks held together by the gluon-gluon interaction into the form of a string)
Interactions treated in the Reggeon-Pomeron framework
each of the two hadrons splits into 2 colored partons  combination into 2 colourless chains  2 back-to-back jets
each jet is then hadronized into physical hadrons

## Slide 9: DPM
single Pomeron exchange
Parton and color concepts, Topological expansion of QCD, Duality
color strings to be “hadronized”
- momentum distribution functions
- fragmentation functions
single chain diagram
two-chain diagram
Reggeon exchange

## Slide 10: Hadron-hadron collisions: chain examples
Leading two-chain diagram in DPM
for p-p scattering
The color (red, blue, and green) and quark combination shown in the figure is just one of the allowed possibilities
Leading two-chain diagram in DPM
for pbar-p scattering
The color (red, antired, blue, antiblue, green, and antigreen) and quark combination shown in the figure is just one of the allowed possibilities
momentum fraction

## Slide 11: Hadron-hadron collisions: chain examples
Leading two-chain diagram in DPM
for +-p scattering
The color (red, antired, blue, and green) and quark combination shown in the figure is just one of the allowed possibilities
Single chain diagram in DPM
for +-p scattering
The color (red, antired, blue, and green) and quark combination shown in the figure is just one of the allowed possibilities
s ~ 1/√s

## Slide 12: Hadronization example
q-q and qq-qq
pairs generation

## Slide 13: DPM and hadronization
from DPM:
Number of chains
Chain composition
Chain energies and momenta
Diffractive events
Almost No Freedom
Chain hadronization
Assumes chain universality
Fragmentation functions from hard processes and e+e− scattering
Transverse momentum from uncertainty considerations
Mass effects at low energies
The same functions and (few) parameters for all reactions and energies

## Slide 14
+ + p  Ch+/Ch- + X (250 GeV/c)
Inelastic hN interactions: examples
+ + p  + + X (6 & 22 GeV/c)
6 GeV
22GeV
M.E. Law et. Al, LBL80 (1972)
Connected points: FLUKA
Symbols w. errors : DATA
Positive hadrons X2
Negative hadrons
Dots: Exp. Data
Histos : FLUKA

## Slide 15: PEANUT
Target nucleus description (density, Fermi motion, etc)
Preequilibrium stage
with current exciton configuration and excitation energy
(all non-nucleons emitted/decayed + all nucleons below 30-100 MeV)
Glauber-Gribov cascade with formation zone
Generalized IntraNuclear cascade
Evaporation/Fragmentation/Fission model
γ de-excitation
t (s)
10-23
10-22
10-20
10-16
NB: above 5 GeV PEANUT is not the default and must be explicitly selected!

## Slide 16: WARNING
PEANUT has been extended to cover the whole energy range in late 2006
A less refined GINC model is available for projectile momenta above about 5 GeV/c, and was the only choice until recently
However: the extended peanut is NOT yet the default, mainly because of some ambiguity in the definition of quasi-elastic cross sections.
To activate PEANUT at all energies:
PHYSICS 1000. 1000. 1000. 1000. 1000. 1000. PEATHRESH

## Slide 17
Nucleon Fermi Motion
Fermi gas model: Nucleons = Non-interacting Constrained Fermions Momentum distribution for k up to a (local) Fermi momentum kF(r) given by The Fermi energy (kF  1.36 fm, PF  260 MeV/c, EF  35 MeV, at nuclear max. density) is customarily used in building a self-consistent Nuclear Potential
Depth of the potential well  Fermi Energy + Nuclear Binding Energy

## Slide 18: Positive kaons as a probe of Fermi motion

## Slide 19
(Generalized) IntraNuclear Cascade
Some assets of the full GINC as implemented in FLUKA (PEANUT):
  Nucleus divided into 16 radial zones of different density, plus 6 outside the nucleus to account for nuclear potential, plus 10 for charged particles
  Different nuclear densities (and Fermi energies) for neutrons and protons (shell model ones for A16)
  Nuclear (complex) optical potential  curved trajectories in the mean nuclear+Coulomb field (reflection, refraction)
  Updating binding energy (from mass tables) after each particle emission
  Multibody absorption for p+/0/- K-/0 m-
  Exact energy-momentum conservation including the recoil of the residual nucleus and experimental binding energies
  Nucleon Fermi motion including wavepacket-like uncertainty smearing, (approximate) nucleon-nucleon, and r  Ef(r) correlations
  Quantum effects (mostly suppressive): Pauli blocking, Formation zone, Nucleon antisymmetrization, Nucleon-nucleon hard-core correlations, Coherence length

## Slide 20
hA at high energies: Glauber-Gribov cascade with formation zone
Glauber cascade
  Quantum mechanical method to compute Elastic, Quasi-elastic and Absorption hA cross sections from Free hadron-nucleon scattering + nuclear ground state
  Multiple Collision expansion of the scattering amplitude
Glauber-Gribov
  Field theory formulation of Glauber model
  Multiple collisions  Feynman diagrams
  High energies: exchange of one or more Pomerons with one or more target nucleons (a closed string exchange)
Formation zone (=materialization time)

## Slide 21: Gribov interpretation of Glauber multiple collisions
Glauber-Gribov model = Field theory formulation of Glauber model
Multiple collision terms Feynman graphs
At high energies : exchange of one or more Pomerons with one or more target nucleons
In the Dual Parton Model language (neglecting higher order diagrams):
Interaction with n target nucleons  2n chains
  Two chains from projectile valence quarks + valence quarks of one target nucleon 2 valence-valence chains
  2(n-1) chains from sea quarks of the projectile + valence quarks of target nucleons 2(n-1) sea-valence chains
The absorption cross section is just the integral in the impact parameter plane of the probability of getting at least one non-elastic hadron-nucleon collision, and it is naturally written in a mutliple collision expansion
with the overall average number of collisions given by

## Slide 22: Chain examples
Leading two-chain diagram in DPM
for p-A Glauber scattering with 4 collisions
The color (red, antired, blue, antiblue, green, and antigreen) and quark combination shown in the figure is just one of the allowed possibilities
Leading two-chain diagram in DPM
for +-A Glauber scattering with 3 collisions
The color (red, antired, blue, antiblue, green, and antigreen) and quark combination shown in the figure is just one of the allowed possibilities

## Slide 23: Formation zone
Naively: “materialization" time
Qualitative estimate:
Particle proper time
Going to the nucleus system
Condition for possible re-interaction inside a nucleus:
In the frame where p|| =0
J.Ranft applied the concept, originally proposed by Stodolski, to hA and AA nuclear int.
Classical INC will never work

## Slide 24: no Glauber, no formation zone
Rapidity distributions of charged particles produced in 250 GeV + collisions on Aluminum (left) and Gold (right)
Points: exp. data (Agababyan et al., ZPC50, 361 (1991))
Positive
Negative
+
Positive
Negative
+

## Slide 25: no Glauber, yes formation zone
Rapidity distributions of charged particles produced in 250 GeV + collisions on Aluminum (left) and Gold (right)
Points: exp. data (Agababyan et al., ZPC50, 361 (1991))
Positive
Negative
+
Positive
Negative
+

## Slide 26: yes Glauber, no formation zone
Rapidity distributions of charged particles produced in 250 GeV + collisions on Aluminum (left) and Gold (right)
Points: exp. data (Agababyan et al., ZPC50, 361 (1991))
Positive
Negative
+
Positive
Negative
+

## Slide 27: yes Glauber, yes formation zone
Rapidity distributions of charged particles produced in 250 GeV + collisions on Aluminum (left) and Gold (right)
Points: exp. data (Agababyan et al., ZPC50, 361 (1991))
Positive
Negative
+
Positive
Negative
+

## Slide 28: Nonelastic hA interactions at high energies: examples
Recent results from the HARP experiment
12.9 GeV/c p on Al
+ production
at different angles
Double differential + production for p C interactions at 158 GeV/c, as measured by NA49 (symbols) and predicted by FLUKA (histograms)

## Slide 29: Double differential pion production
data from BNL910 experiment

## Slide 30: Double differential pion production
data from BNL910 experiment

## Slide 31: Double differential pion production

## Slide 32: Pions: nuclear medium effects
Free π N interactions  |  | Non resonant channel
 |  | P-wave resonant Δ production
Assuming for the free resonant  a Breit-Wigner form with width F
Δ in nuclear medium |  | decay | elastic scattering, charge exchange
 |  | reinteraction |  Multibody pion absorption
An ``in medium'' resonant  (Ares) can be obtained adding to F the imaginary part of the (extra) width arising from nuclear medium
quasielastic scattering, two and three body absorption
The in-nucleus tA takes also into account a two-body s-wave absorption sA derived from the optical model
(Oset et al., NPA 468, 631)

## Slide 33: Pion absorption
Pion absorption cross section on Gold and Bismuth in the  resonance region (multibody absorption in PEANUT)
Emitted proton spectra at different angles , 160 MeV + on 58Ni
Phys. Rev. C41,2215 (1990)
Phys. Rev. C24,211 (1981)
Proton spectra extend up to 300 MeV

## Slide 34: Coalescence
High energy light fragments are emitted through the coalescence mechanism: “put together” emitted nucleons that are near in phase space.
Example : double differential t production from 542 MeV neutrons on Copper
Warning: coalescence is OFF by default
Can be important, ex for . residual nuclei.
To activate it:
PHYSICS 1. COALESCE
If coalescence is on, switch on Heavy ion transport and interactions (see later)

## Slide 35: Preequilibrium emission
For E >  production threshold  only (G)INC models
At lower energies a variety of preequilibrium models
Two leading approaches
The quantum-mechanical multistep model:
Very good theoretical background
Complex, difficulties for multiple emissions
The semiclassical exciton model
Statistical assumptions
Simple and fast
Suitable for MC
Statistical assumption:
any partition of the excitation energy E* among N, N = Nh +Np, excitons has the same probability to occur
Step: nucleon-nucleon collision with Nn+1=Nn+2 (“never come back approximation)
Chain end = equilibrium = Nn sufficiently high or excitation energy below threshold
N1 depends on the reaction type and cascade history

## Slide 36: Thin target example
Angle-integrated 90Zr(p,xn) at 80.5 MeV
The various lines show the total, INC, preequilibrium and evaporation contributions
Experimental data from
M. Trabandt et al., Phys. Rev. C39, 452 (1989)

## Slide 37
Thin target examples
p + 90Zr  p + X (80 MeV)
p + Al  - + X (4 GeV/c)

## Slide 38: Equilibrium particle emission (evaporation, fission and nuclear break-up)
Probability per unit time of emitting a particle j with energy E
Probability per unit time of fissioning
From statistical considerations and the detailed balance principle, the probabilities for emitting a particle of mass mj, spin Sj,ħ and energy E, or of fissioning are given by:
(i, f for initial/final state, Fiss for fission saddle point)
ρ’s: nuclear level densities
U’s: excitation energies
Vj’s: possible Coulomb barrier for emitting a particle type j
BFiss: fission barrier
Qj’s: reaction Q for emitting a particle type j
σinv: cross section for the inverse process
Δ’s: pairing energies
Neutron emission is strongly favoured because of the lack of any barrier
Heavy nuclei generally reach higher excitations because of more intense cascading

## Slide 39
Equilibrium particle emission
Evaporation: Weisskopf-Ewing approach
  ~600 possible emitted particles/states (A<25) with an extended evaporation/fragmentation formalism
  Full level density formula with level density parameter A,Z and excitation dependent
  Inverse cross section with proper sub-barrier
  Analytic solution for the emission widths (neglecting the level density dependence on U, taken into account by rejection
  Emission energies from the width expression with no. approx.
Fission: past, improved version of the Atchison algorithm, now
  fis based of first principles, full competition with evaporation
  Improved mass and charge widths
  Myers and Swiatecki fission barriers, with exc. en. Dependent level density enhancement at saddle point
Fermi Break-up for A<18 nuclei
  ~ 50000 combinations included with up to 6 ejectiles
 de-excitation: statistical + rotational + tabulated levels

## Slide 40: Residual Nuclei
The production of residuals is the result of the last step of the nuclear reaction, thus it is influenced by all the previous stages
Residual mass distributions are very well reproduced
Residuals near to the compound mass are usually well reproduced
However, the production of specific isotopes may be influenced by additional problems which have little or no impact on the emitted particle spectra (Sensitive to details of evaporation, Nuclear structure effects, Lack of spin-parity dependent calculations in most MC models)

## Slide 41: Example of fission/evaporation
1 A GeV 208Pb + p reactions Nucl. Phys. A 686 (2001) 481-524
Quasi-elastic
Spallation
Deep spallation
Fission
Fragmentation
Evaporation
Data
FLUKA
FLUKA after cascade
FLUKA after preeq

## Slide 42: Residual nuclei
42
Experimental and computed
residual nuclei mass distribution
for Ag(p,x)X at 300 GeV
Data from
Phys. Rev. C19 2388 (1979) and
Nucl. Phys. A543, 703 (1992)
The fragmentation model has much improved the FLUKA predictions
Also for A-A interactions
Warning: fragmentation is OFF by default, because it is a cpu-eater. It is NECESSARY to activate it for activation studies:
PHYSICS 3. EVAPORAT
If fragmentation is on, switch on Heavy ion transport and interactions (see later)
Notes: 42

## Slide 43: Summary of relevant input cards
to use the more refined PEANUT model for h-A reactions also above 5GeV
to enable evaporation of heavy fragments
to enable coalescence (at the cascade stage of the reaction, before pre-equilibrium)
etc.
PHYSICS 3. EVAPORAT
PHYSICS 1. COALESCE
PHYSICS 1000. 1000. 1000. 1000. 1000. 1000. PEATHRESH

## Slide 45: Glauber Cascade
Quantum mechanical method to compute all relevant hadron-nucleus cross sections from hadron-nucleon scattering:
and nuclear ground state wave function i
Scattering
Elastic
Total
Absorption probability over a given b and nucleon configuration
Absorption (particle prod.)