## Slide 1: EM interactions
Beginners’ FLUKA Course

## Slide 2: Topics
General settings
Interactions of leptons/photons
  Photon interactions
    Photoelectric
    Compton
    Rayleigh
    Pair production
    Photonuclear
    Photomuon production
  Electron/positron interactions
    Bremsstrahlung
    Scattering on electrons
  Muon interactions
    Bremsstrahlung
    Pair production
    Nuclear interactions
Ionization energy losses
  Continuous
  Delta-ray production
Transport
  Multiple scattering
  Single scattering
These are common to all charged particles,
although traditionally associated with EM

## Slide 3: E-M FLUKA (EMF) at a glance
EMF EMF-OFF
Energy range for e+ , e- ,  : 1 keV (100 eV for  )- 1000 TeV
Full coupling in both directions with hadrons and low-energy neutrons
Energy conservation within computer precision
Up-to-date  cross section tabulations from EPDL97 database
EMF is activated by default….and with most DEFAULTS options,
except: EET-TRAN, NEUTRONS, SHIELDING
To de-activate EMF:
With EMF-OFF, E.M. energy is deposited on the spot
Consider also the DISCARD command
Production and transport of optical photons (Cherenkov, scintillation) is implemented. Since it needs user coding, it is not treated in this beginners course

## Slide 4: Transport thresholds
EM particles are transported until their energy falls below a preset threshold. In FLUKA, this energy threshold can be set REGION BY REGION.
HOW to choose?
It depends on the “granularity” of the geometry and/or of the scoring mesh and on the “interest” in a given region. Energy/range tables are very useful (see for instance http://physics.nist.gov )
Warning 1: to reproduce correctly electronic equilibrium, neighboring regions should have the same electron energy (NOT range) threshold. To be kept in mind for sampling calorimeters
Warning 2 : Photon thresholds should be lower than electron thresholds (photons travel more)
Warning 3: low thresholds are CPU eaters
EMFCUT e±Thresh Thresh 0.0 Reg1 Reg2 Step

## Slide 5: Production Thresholds
Let’s introduce a concept that is treated again in the discussion of ionization energy losses: the separation between CONTINUOUS and DISCRETE energy deposition:
The simulation of all atomic interaction processes is not possible in all-purposes MCs, because
  the modeling of very low energy transfer would need detailed atomic/molecular physics
  the CPU time would diverge
  1) ONLY interactions resulting in a “substantial” energy transfer are simulated explicitly
  2) All other interactions are “condensed” in a continuous energy loss along the particle step
Condition 1) is implemented by setting a threshold for the energy of the produced secondary particles (“delta rays”) :
SDUM = PROD-CUT
The production threshold is also used as lowest energy limit to prepare cross section tabulations at initialization stage.

## Slide 6: Production Thresholds -II
EMFCUT e±Thresh Thresh Fudgem Mat1 Mat2 Step PROD-CUT
BY MATERIAL !
Fudgem is related to multiple scattering. = 0 below ≈ 10 keV , = 1 above
MUST be set, if the field is empty  0
For electromagnetic interactions:
Warning 1: production and transport thresholds are set by default, depending on the DEFAULTS card. DO NOT RELY on them, choose those best suited for your problem
Warning 2: if prod-cut < transport cut, CPU is wasted in producing/dumping particles on spot. Sometimes it could be convenient to define several “equal” materials with different production thresholds (and different names)
Warning 3: if prod-cut > transport cut , the program automatically increases the transport threshold , because it cannot transport a particle that it is not supposed to handle.

## Slide 7
Photon interactions

## Slide 8: Photoelectric effect
Detailed treatment of | Fluorescence
Photoelectron | Angular distribution
Approximate | Auger effect
Effect of photon | Polarization
EMFFLUO Flag Mat1 Mat2 Step
Fluorescence after photoelectric is activated only with a subset of DEFAULTS
CPU time vs. precision in small granularity
To activate/deactivate it:
Warning: check consistency with production/transport thresholds
Flag > 0: Activate Flag < 0: De-activate

## Slide 9: Compton and Rayleigh
Account for atomic bonds using inelastic Hartree-Fock form factors (very important at low E in high Z materials)
NEW : Compton with atomic bonds and orbital motion (as better alternative to form factors)
  Atomic shells from databases
  Orbital motion from database + fit
  Followed by fluorescence
Account for effect of photon polarization
EMFRAY Flag Reg1 Reg2 Step
Inelastic Form Factors, Compton profile and Rayleigh scattering are activated only with a subset of DEFAULTS .
To activate/deactivate:
Look in the manual for further details

## Slide 10: Compton profile examples
green = free electron
blue = binding with form factors
red = binding with shells and orbital motion
50 keV  on Au
E’/E
500 keV  on Au
E’/E
Larger effect at very low energies, where, however, the dominant process is photoelectric.
Visible: shell structure near E’=E, smearing from motion at low E’
E’/E
E’/E
E/Z ds/dE’
E/Z ds/dE’

## Slide 11: Polarization
POLARIZA Pcosx Pcosy Pcosz Flag1 Fraction Flag2
By default, source photons are NOT polarized. Polarization can be set by
Flag1 >= 1  Pol. direction orthogonal to direction of motion,
Fraction + flag2  fraction of polarized/unpolarized or polarized/orthogonally polarized photons (see the manual for further details)
Effect of photon polarization
Deposited dose
by 30 keV photons on Water
at 3 distances from beam axis
as a function of penetration depth for 3 orientations wrt the polarization direction
Z[cm]
Dose [Gy r-1]

## Slide 12: Pair Production
Angular and energy distribution of e+,e- described correctly (no “fixed angle” or similar approximation)
No approximations near threshold
Extended to 1000 TeV taking into account the LPM (Landau-Pomeranchuk-Migdal) effect
Differences between emitted e+ and e- at threshold accounted for

## Slide 13: Photonuclear interactions
Giant Resonance interaction
Quasi-Deuteron effect
Delta Resonance production
Vector Meson Dominance (  r, F mesons) at high energies
Photon-nucleus interactions in FLUKA are simulated over the whole energy range, through different mechanisms:
Nuclear effects on the initial state (i.e. Fermi motion) and on the final state (reinteraction / emission of reaction products) are treated by the FLUKA hadronic interaction model (PEANUT)  INC + pre-equilibrium + evaporation/fission/breakup
The (small) photonuclear interaction probability can be enhanced through biasing (see command LAM-BIAS)

## Slide 14: Photonuclear interactions: options
PHOTONUC Flag Mat1 Mat2 Step
Photonuclear interactions are NOT activated with any default
To activate them:
Since the photonuclear cross section is very small, PHOTONUC should be always accompanied by LAM-BIAS with SDUM = blank (see lecture on biasing)
LAM-BIAS 0.0 Factor Mat PHOTON
Applications:
electron accelerator shielding and activation
neutron background by underground muons (together with muon
photonuclear interactions (option MUPHOTON)
Flag controls activation of interactions, with the possibility to select a subset of the photonuclear mechanisms
Notes: 14

## Slide 15: Photonuclear Interactions: benchmark
Yield of neutrons per incident electron as a function of initial e- energy. Open symbols: FLUKA, closed symbols: experimental data (Barber and George, Phys. Rev. 116, 1551-1559 (1959))
Left: Pb, 1.01 X0 (lower points) and 5.93 X0 (upper)
Right: U, 1.14 and 3.46 X0

## Slide 16: Photonuclear int.: example
Reaction:
208Pb(g,x n)
20  Eg  140 MeV
Cross section for multiple neutron emission as a function of photon energy, Different colors refer to neutron multiplicity  n , with 2  n  8
Symbols: exp. data (NPA367, 237 (1981) ; NPA390, 221 (1982) )
Lines: FLUKA

## Slide 17: Photomuon production
PHOTONUC Flag Lambias 0.0 Mat1 Mat2 Step MUMUPAIR
Muon pair production by photons is NOT activated with any default
To activate it:
Flag controls activation of interactions, with the possibility to select a subset of the photomuon mechanisms (coherent, incoherent, inelastic...)
Biasing of photomuon production can be done directly with this card, setting WHAT(2)

## Slide 18
Electron/Positron interactions

## Slide 19: Bremsstrahlung
Energy-differential cross sections based on the Seltzer and Berger database, interpolated and extended to a finer energy mesh, tip, and larger energies
Finite value at tip energy (tip == max energy of photon)
Extended to 1000 TeV taking into account the LPM (Landau-Pomeranchuk-Migdal) effect
Soft photon suppression (Ter-Mikaelyan) polarization effect
Special treatment of positron bremsstrahlung with ad hoc spectra at low energies
Detailed photon angular distribution fully correlated to energy

## Slide 20: Bremsstrahlung: benchmark
2 MeV electrons on Iron,
Bremsstrahlung photon spectra
measured (dots)
and
simulated (histos)
at three different angles

## Slide 21: Bremsstrahlung: benchmark II
12 and 20.9 MeV electrons on a W-Au-Al target,
bremsstrahlung photon spectra in the forward direction
measured (dots) and simulated (histos)

## Slide 22: Bremsstrahlung: benchmark III Esposito et al., LNF 93-072
ADONE storage ring
1.5 GeV e-
Bremss. on the residual gas in the straight sections
Measured with TLD’s matrices at different distances from the straight Section
Here: dose vs. horizontal position at different vertical positions , d=218cm

## Slide 23: Other e± interactions
At rest and in flight according to Heitler.
In annihilation at rest, account for mutual polarization of the two photons
Acolinearity of the photons at rest can be requested, with
annihilation photon energies spread out
Positron Annihilation
Scattering
e+ : Bhabha
e- : Møller

## Slide 24: Electron scattering:
Transmitted (forward) and backscattered (backward) electron angular distributions for 1.75 MeV electrons on a 0.364 g/cm2 thick Copper foil Measured (dots) and simulated (histos) data

## Slide 25
The ATLAS EM “accordion” calo (standalone test beams)
Energy resolution 10-100 GeV:
Detail of the FLUKA geometry and
287 GeV
electron
beam
deposited energy
Stars : fluka
Dots: expt. (RD3 collab.)
impact position
response vs. electron impact position

## Slide 26
Muon interactions

## Slide 27: Bremsstrahlung and pair production
Bremsstrahlung: implemented in FLUKA including the effect of nuclear form factors
Pair Production: implemented
At high energies, bremsstrahlung and pair production
are important also for muons and charged hadrons.
For instance, in Lead the muon energy loss is
dominated by these processes above 300 GeV.
For muons and all charged hadrons:
PAIRBREM Flag e±Thresh Thresh Mat1 Mat2 Step
Activation of these processes and thresholds of EXPLICIT  and e± production depend on the DEFAULTS chosen. They are controlled by the card
Below threshold, energy loss is accounted for in a continuous approximation

## Slide 28: Energy Deposition spectrum in the Atlas tile-calorimeter prototype
ionization
Bremsstrahlung +
Pair production
300 GeV muons on iron + scintillator structure

## Slide 29: Energy Deposition spectrum in the Atlas tile-calorimeter prototype
300 GeV muons on iron + scintillator structure
Muon energy [GeV]
Muon
energy [GeV]

## Slide 30: Muon Photonuclear Reactions
The cross section can be factorized (following Bezrukov-Bugaev) in
virtual photon production and photon-nucleus reaction
Nuclear screening is taken into account
Only Virtual Meson Interactions are modeled, following the
FLUKA meson-nucleon interaction models
Nuclear effects are the same as for hadron-nucleus interactions
Schematic view of a m hadronic interaction.
The interaction is mediated by a virtual photon.
The final state can be more complex

## Slide 31: Muon photonuclear: options
LAM-BIAS 0.0 Factor Mat MUON+ MUON-
 photonuclear interactions are NOT activated with any default
To activate them:
Since the  photonuclear cross section is very small, MUPHOTON should be always accompanied by LAM-BIAS ( see lecture on biasing)
Flag controls activation of interactions, with the possibility to simulate the interaction without explicit production and transport of secondaries
(this gives the correct muon energy loss/ straggling)
MUPHOTON Flag 0.0 0.0 Mat1 Mat2 Step

## Slide 32: Muon-induced neutron background in underground labs
Neutron production rate as a function of muon energy
Stars+line : FLUKA simulation with a fit to a power law.
Exp. points:
abscissa average  energy
at the experiment's depth:
20 m.w.e.
25 m.w.e.
C) 32 m.w.e. (Palo Verde)
D) 316 m.w.e.
E) 750 m.w.e.
F) 3650 m.w.e. (LVD)
G) 5200 m.w.e. (LSD)
m.w.e. = meter of water equivalent
PRD64 (2001) 013012

## Slide 33: Muon Capture (1)

## Slide 34: Muon Capture (2)

## Slide 35
Electromagnetic dissociation
Note: Electromagnetic dissociation is already relevant for interactions of
few GeV/n ions in heavy targets.

## Slide 36
Electromagnetic dissociation - Benchmarks
Electromagnetic dissociation cross sections (total, 1nX, 2nX) for 30GeV/n Pb ions on
Al, Cu, Sn, and Pb targets.
FLUKA: lines (calculated cross section as a function of target charge)
Exp. data: M.B.Golubeva et al.

## Slide 37: 158 GeV/n Pb ion fragmentation
Fragment charge cross section for 158 AGeV Pb ions on various targets. Data (symbols) from NPA662, 207 (2000), NPA707, 513 (2002) (blue circles) and from C.Scheidenberger et al. PRC70, 014902 (2004), (red squares), yellow histos are FLUKA (with DPMJET-III) predictions: purple histos are the electromagnetic dissociation contribution

## Slide 38
Spare slides

## Slide 39: Electromagnetic dissociation: example
28Si(g,tot) as recorded in FLUKA database, 8 interval Bezier fit as used for the Electromagnetic Dissociation event generator.