## Slide 1: Highlights on advanced topics
Beginners’ FLUKA Course

## Slide 2
This is not the end …
As said in the first day, most applications can be run through data-cards only, exploiting the FLUKA built-in capacities
Sometimes, more is needed…
A set of templates User Routines is provided in the $FLUPRO/usermvax directory
These can be modified by the user to fit his input/output needs
We’ll give here some hints of what can be done, more can be found in the manual, in the fluka-discuss archive, or
at the FLUKA workshop and advanced course
to be held in Portugal, autumn 2010

## Slide 3
Implementing customized beam distributions - 1
11% above 30 sigma
16% above 15 sigma
LHC proton beam at the Dispersion Suppressor entrance

## Slide 4
Implementing customized beam distributions - 2
Input card: SOURCE User routine: $FLUPRO/usermvax/source.f
In source.f
you can sample beam particle position, direction, and energy
from an external file or any (analytic or numerical) distribution
you can assign different weights to primary particles
you can load reaction products in the same primary history
parameters input in the SOURCE card are available
to be linked in one’s own executable !
a BEAM card with a momentum/energy higher than the maximum one is still needed
for initialization purposes (to define the tabulation limit)

## Slide 5
The two magnetic lenses (blue in the sketch) align positive mesons towards the Decay tunnel, so that neutrinos from the decay are directed to GranSasso, 730~km away
Negative mesons are deflected away
The lenses have a finite energy/angle acceptance
Implementing magnetic field - 1
CERN Neutrino to Gran Sasso

## Slide 6
Implementing magnetic field - 2
Magnetic field intensity in the CNGS horn
A current ≈150kA, pulsed, circulates through the
Inner
and
Outer
conductors
The field is toroidal,
B1/R
Input card: ASSIGNMA User routine: $FLUPRO/usermvax/magfld.f
to be linked in one’s own executable !

## Slide 8
1 event
USRBIN R-Z
SUBROUTINE MAGFLD ( X, Y, Z, BTX, BTY, BTZ, B, NREG, IDISC )
IF ( NREG .EQ. NRHORN ) THEN
RRR = SQRT ( X**2 + Y**2 )
BTX =-Y / RRR
BTY = X / RRR
BTZ = ZERZER
B = 2.D-07 * CURHOR / 1.D-02 / RRR
END IF
Focused
De-focused
Escaping…many
Implementing magnetic field - 4
In magfld.f
you can define the magnetic field analytically or
by interpolating an external map
charged particle tracks in the CNGS geometry

## Slide 9
Implementing customized scoring - 1
beam crossing in ATLAS

## Slide 10
Implementing customized scoring - 2
Input card: USERDUMP User routine: $FLUPRO/usermvax/mgdraw.f
In mgdraw.f
you can get particle trajectories and (continuous and local) energy losses
you can go over reaction products
you can access information at each boundary crossing, particle step,
energy deposition event, interaction
to be linked in one’s own executable !
In mdstck.f (for which no activating card is needed) as well,
with the additional – dangerous – possibility of influencing
the subsequent transport of secondaries

## Slide 11
Implementing customized scoring-3
Input card: USERWEIG User routines: $FLUPRO/usermvax/comscw.f
$FLUPRO/usermvax/fluscw.f
In comscw.f
you can apply a user defined weight (even discard) on deposited energy, stars or residual nuclei
you can extract information (and dump it on a file) about the
involved particles
to be linked in one’s own executable !
In fluscw.f
same as comscw.f for fluence scoring.

## Slide 12
Implementing customized flags
No input card User routines: $FLUPRO/usermvax/stuprf.f
$FLUPRO/usermvax/stupre.f
In stuprf.f
you can keep track of the particle origin
to be linked in one’s own executable !
stupre.f applies in case of electrons, photons and positrons
identification of ancestors of muon-neutrinos reaching Gran Sasso
ancestor as exiting the target
parent decaying in nm