## Slide 1: Exercise 7: Importance biasing
Beginners FLUKA Course

## Slide 2: Exercise 7: Importance biasing
-50
-60
60
50
10
250
Concrete shield
240
Create a new directory ex7 and download the ex5.inp, renamed it to ex7.inp
Step 1:
change targets back to H2O/Al/Pb
add a 240 cm thick concrete shield around the target
calculate neutron fluence inside the shield
in region-independent mesh (USRBIN) create a contour plot with FLAIR
Step 2:
split lateral shield into 6 layers of 40 cm thickness each and assign region importance factor to each layer such that the importance increases between adjacent layers by a factor of two
calculate again the neutron fluence inside the shield, create contour plot and compare to case without region importance biasing
Tip: you can create a #define BIAS variable and enclose the BIASING cards with #if BIAS…#endif cards. Then create a second run in the Run Frame with the BIAS disabled
Concrete: (mass fraction)
Hydrogen 0.01 Aluminum 0.034
Carbon 0.001 Silicon 0.337
Oxygen 0.529 Potassium 0.013
Sodium 0.016 Calcium 0.044
Magnesium 0.002 Iron 0.014
Density: 2.42g/cm3
H2O
Pb
Al

## Slide 3: Exercise 7 – Importance biasing
Result